Finding output impedance for a circuit

Assume with the circuit below that the output impedance is wanted from the marked voltage node.

Step 1:  Remove the input V6 and set it to ground or the input values to zero.

Step 2:  Replace the load resistor, R6 with a test source (Current or Voltage for out example) and place V marker and I marker at the node you want to find the resistance.

Step 3:  Simulate using an AC sweep and plot the current coming out of the source V8.

Step 4.  Determine the output impedance vs frequency value =>

a.  The following plot comes up of I and V on it.

Note that the current is I(V8) and the voltage is V(x3:d) =>

Get to the Modify Trace window (either by double clicking on the variable I(V8) or a different variable or through the menus.  Replace the Trace Expression with V/I to give you the graph of resistance vs frequency.  Trace Expression:  V(x3:d)/I(V8) {your node voltages will be different than mine}.  The resultant plot should look something like the form below:

where this shows Rout = 2.62 when it is under 200 Hz.

Plotting to create a VGS x-axis:

Step 1.  Create graph of Vout vs VG.  Double click on the x-axis to get the following:

Under the x-axis tab => click on axis variable.

Change the Trace Expression to be the VG node – VS node (depends on your circuit).  Click OK and this changes the axis to be the above expression instead of just VG.