ANALYZE:
                 A tool to aid in the analysis and verification
                            of asynchronous circuits



HISTORY



Current design practices heavily depend on automated tool support for the
time consuming tasks of circuit and system analysis and synthesis.
Asynchronous design practices are a fledgling application to today's
technology which ultimately require the same, if not greater, tool
sophistication to achieve commercial credibility and acceptance.
Fortunately, the hierarchical and modular nature of asynchronous design
lends itself particularly well to synthesis and verification formalism and
algorithms.  This is a tool which helps to fill the tool need in the domain
of formal asynchronous circuit and system verification.

Although asynchronous systems can be based on formal handshake semantics,
"equality" between behavioral descriptions and implementations has been
difficult to formally define.  Milner's work on CCS -- "Calculus of
Communicating Systems" -- has helped me formalize and understand
equalities.  Bisimulation, and a property I define as "conformance" can be
combined to formally prove satisfaction between arbitrary hierarchies of
asynchronous components and systems and their specifications.

This tool uses CCS as an input language to analyze asynchronous circuits
and verify they satisfy the specification.  ANALYZE is in its infancy, and
is very incomplete at this stage.  The tool is coded using efficient model
checking techniques.  Bisimulation and Trace equivalences are the
foundational work between specification and implementation.  Temporal model
checking, which can be used to validate the initial specification or an
implementation, must be done using other tools such as the Concurrency
Workbench (CWB) or the Concurrency Factory.



WHAT ANALYZE DOES



ANALYZE will take a CCS description and do a number of checks and
expansions which are not possible using standard CCS syntax and expansion
laws.  This allows circuits to be analyzed in 1: speed-independent
(arbitrary delay of devices), 2: delay-insensitive (arbitrary delay of
devices and interconnections), and 3: burst (speed-independent with
stability) modes.  ANALYZE performs static checks of the implementation to
ensure correct interconnection, and some specification and application
requirements.  Analyze will also generate CWB compatible output of
minimized agents in standard normal form.

When both a specification and implementation are supplied, the
implementation will be verified for satisfaction (called conformance) to
the specification.  Verification uses both bisimulation and trace
formalisms.



GETTING STARTED



You should formalize yourself with the syntax and usage of CCS.  See
Milner's book, and Liu's thesis for examples.  The syntax is the same as in
the workbench, but only the agent definition binding "bi" is supported.
Operator precedence is: . > () > \ {} [] > +
This is somewhat different from the Concurrency Workbench, but is more
suitable to specifying hardware components.


USE



CCS agents must be placed in a file.  Agents can be implementations or
specifications, and the order of definitions in irrelevant.  ANALYZE will
read the file, parsing and loading the agents into a hash table.  You can
then build composite agents checking for correct construction and verify
them.

ANALYZE is written in common-lisp.  The command (load "load-analyze.lisp")
will load all the necessary files into your lisp system.  Please compile
all the files (load "compile-analyze.lisp") the first time you load them!

There are only four functions in the current implementation that you must
know to run ANALYZE:

PARSE-AGENTS
  Has one required formal parameter, the file name which contains the agent
   definitions to load.
  A second optional parameter, if non-nil will read the agent into the
   hash table without clearing it first.  (So you can add in agent
   definitions from multiple files.)

SHOW-ANALYSIS-MODE
  This function shows what mode the tool is in.  It allows you to select
   between burst-mode, speed-independent, and delay-insensitive
   verifications.  (Hopefully annotations will be implemented soon to allow
   mixed-mode analysis.)  This function informs you of other support
   functions to change the analysis mode. 

ANALYZE
  This function prints out verification and/or minimization results, and
   returns the name of the new agent which is generated as a result of the
   analysis.
  This function has a single required argument, the name of the agent to be
   analyzed.
  If a second optional argument is included, it is the definition of the
   specification as a CCS process.  When this argument is present, the
   implementation in the first argument will be verified for conformance to
   the specification.  If you do not supply this argument, the
   implementation will be minimized into standard normal form.  Standard
   normal form looses the structure of the implementation.  Verification is
   faster than minimization so it is typically used.

PRINT-AGENT
  This function prints the agent to the screen or a file.
  The first argument is the name of the agent to print.
  The optional second parameter is a file name.

TRACE-CONVERT
  This function converts a bisimilar process into a trace process.
   This occurs by collapsing all taus via the trace "hiding" formalism.
  This function takes one argument which is the name of a canonical process.
   (You may need to run the analyze function to get a canonical process.)
  Return value is a list where the first element is the name of the trace
   process, the second element is the state size of the process.


Under burst-mode analysis, it is possible to have a null output transition.
It is also possible that the burst-mode stability requirement is necessary
for these transitions.  Hence, a specification can be annotated by the
special transition 'burstModeStable which will force the circuit to
stabilize at the end of the input burst (and after the null output burst).



SAMPLE SESSION



There are two "gotcha's" that you need to remember when running this
system.  First, agent and signal names are referred to as lisp identifiers.
This results in efficient manipulating of state and signal names.  However,
as lisp generally assumes no case sensitivity, you must quote agent names
which do not contain all uppercase characters.  This is done by bounding
the agent in bars, such as |WeIrD-aGeNt|.  Defining agents as fully
uppercase strings simplifies the user interface because they can simply be
quoted (eg 'c-element) and the Lisp token parser will create an upper-case
identifier to match the upper-case process name.

Secondly, a fresh package is created to store all action and agent names to
assure there are no name conflicts.  All agent names which have been parsed
by ANALYZE are placed into a package called "labels".  The above functions
all assume that the arguments are in the labels package, but if you want to
reference any processes or identifiers in the Lisp reader, you will have to
explicitly state the package name.  For instance, the above agent can be
referenced in the debugger and read-loop as 'labels::|WeIrD-aGeNt|.

This is a sample run verifying a C-element implementation as an example.
Assume that the file c-element.ccs contains the following CCS definitions
of a C-element:

****** the file C-element.ccs ******

***  Here is the specification for a C-element:

bi C-SPEC a.b.'c.C-SPEC + b.a.'c.C-SPEC


*** Here is the definition of a C-element implementation:


bi C-ELEMENT
( AND00[ab/c]			\
| AND00[c/b, ac/c]		\
| AND00[b/a, c/b, bc/c]		\
| OR000[ab/a, ac/b, bc/c, c/d]	\
) \ { ab, ac, bc }


*** These are "library cells" referenced by the C-element.
*** They describe the behavior of the AND and OR gates.


***********************************************************
***	Non-Blocking 3-input OR gate			***
***********************************************************
* a b c inputs d output

bi ORa000  'd.ORa001 + b.ORab00 + c.ORa0c0
bi OR0b00  a.ORab00 + 'd.OR0b01 + c.OR0bc0
bi OR00c0  a.ORa0c0 + b.OR0bc0 + 'd.OR00c1
bi ORab00  a.OR0b00 + b.ORa000 + c.ORabc0 + 'd.ORab01
bi ORa0c0  a.OR00c0 + b.ORabc0 + c.ORa000 + 'd.ORa0c1
bi OR0bc0  a.ORabc0 + b.OR00c0 + c.OR0b00 + 'd.OR0bc1
bi ORabc0  a.OR0bc0 + b.ORa0c0 + c.ORab00 + 'd.ORabc1
bi OR0000  a.ORa000 + b.OR0b00 + c.OR00c0
bi OR0001  'd.OR0000
bi ORa001  a.OR0001 + b.ORab01 + c.ORa0c1
bi OR0b01  a.ORab01 + b.OR0001 + c.OR0bc1
bi OR00c1  a.ORa0c1 + b.OR0bc1 + c.OR0001
bi ORab01  a.OR0b01 + b.ORa001 + c.ORabc1
bi ORa0c1  a.OR00c1 + b.ORabc1 + c.ORa001
bi OR0bc1  a.ORabc1 + b.OR00c1 + c.OR0b01
bi ORabc1  a.OR0bc1 + b.ORa0c1 + c.ORab01


***********************************************************
***	Non-Blocking 2-input AND gate			***
***********************************************************
* a and b are inputs, c is output.

bi AND000  a.ANDa00 + b.AND0b0
bi ANDa00  a.AND000 + b.'c.ANDab1
bi AND0b0  a.'c.ANDab1 + b.AND000
bi ANDab1  a.AND0b1 + b.ANDa01
bi AND0b1  'c.AND0b0 + b.AND001
bi ANDa01  a.AND001 + 'c.ANDa00
bi AND001  a.ANDa01 + b.AND0b1 + 'c.AND000



****** end of the file c-element.ccs ******


You will need to load the analyze binaries into the lisp session.  Do this
with the command:

> (load "load-analyze.lisp")

The '>' is the lisp prompt.  You must be connected to the directory that
contains the analyze source and binary files.  Some lisp systems have a
'cd' function so you can change the connected directory with the focus of
the lisp system.  Otherwise you will need to give path names to the
load-analyze.lisp file, and modify it so that it references the locations
of the source files.  Enter (load "compile-analyze.lisp") the first time
you use the system to ensure good binaries.

We are now ready to verify the circuit!  Following is a transcript of a run,
with an explanation that follows.


****** Here is a transcript of a verification run: ******


> (show-analysis-mode)

;;; Current Mode Settings:
;;;      Speed-Independent Mode (using isochronous forks).
;;;
;;;   Interference errors in unverified cells ignored.
;;;
;;;   Duplicate error printing limit: 4 (1- Error-Limit*)
;;;
;;; Use (delay-insensitive-mode) or (speed-independent-mode)
;;;  to change the wire formalism.
;;; The function (toggle-burst-mode) will set/reset burst-mode analysis.
;;; The function (toggle-unverified-interference) will set/reset these messages.
;;; The function (toggle-workbench-mode) will set/reset workbench agent generation
NIL
> (parse-agents "../examples/dist/c-element.ccs")
24
> (analyze 'c-element)
 
;;;
;;; Parameters set for speed-independent analysis 
;;;
;;; SORT WARNING: Connected, unrestricted input/output `c' in C-element*!
 
 
;;;
;;; The top-level agent contains 36 minimized states
;;;
;;;
;;;   The following are warnings or errors detected during analysis:
;;;        - No specification was found.  Entire agent state set generated.
;;;        - This agent contains computation interference.
;;;          This may be due to incorrect interconnection or
;;;          interface assumptions.  These problems must be removed
;;;          to build a correct implementation.
;;;        - 1 warnings were issued...
;;;
;;; Warning: 
;;;          
;;;          1 errors encountered during creation of agent C-element*-0*-0.
;;;               Do NOT trust the behavior of this agent!
;;;          
;;;          
LABELS::C-ELEMENT*-0*-0|
> (analyze 'c-element 'c-spec)
 
;;;
;;; Parameters set for speed-independent analysis with trace verification
;;;
;;; Generating a trace-determinate specification from C-SPEC .....
;;;   ... minimized spec contains 4 states
;;;   ... successfully generated TD specification with 4 states
;;; Generating and trace verifying C-ELEMENT against St-C-SPEC*^0M3-0M3 .....
;;;
;;; SORT WARNING: Connected, unrestricted input/output `c' in C-ELEMENT*!
;;; ERROR! Computation interference encountered!
;;;     Signal  'ac  in agent C-ELEMENT*
;;;   Trace: (b a 'ab 'c 'bc b 'ab 'bc 'ac)
;;; ERROR! Computation interference encountered!
;;;     Signal  'c  in agent C-ELEMENT*
;;;   Trace: (b a 'ab 'c 'bc b 'ab 'bc 'c)
;;; ERROR! Computation interference encountered!
;;;     Signal  'ac  in agent C-ELEMENT*
;;;   Trace: (b a 'ab 'c 'bc b 'bc 'ab 'ac)
;;; ERROR! Computation interference encountered!
;;;     Signal  'c  in agent C-ELEMENT*
;;;   Trace: (b a 'ab 'c 'bc b 'bc 'ab 'c)
;;; ERROR! Computation interference encountered!
;;;     Signal  'c  in agent C-ELEMENT*
;;;   Trace: (b a 'ab 'c 'ac a 'ab 'ac 'c)
;;; ERROR! Computation interference encountered!
;;;     Signal  'bc  in agent C-ELEMENT*
;;;   Trace: (b a 'ab 'c 'ac a 'ab 'ac 'bc)
;;; Warning: Agent being redefined! (component C-ELEMENT*-6)
;;;          
 
 
;;;
;;; The top-level agent contains 33 unminimized states
;;;
;;;
;;;   The following are warnings or errors detected during analysis:
;;;        - The agent contained computation interference.
;;;          If this is an implementation it is NOT conformant to specification
;;;          Otherwise synchronizations are incomplete to implement the spec.
;;;        - Duplicate error type messages were suppressed.
;;;        - 2 warnings were issued...
;;;
;;; Warning: 
;;;          
;;;          8 errors encountered during creation of agent C-ELEMENT*-0.
;;;               Do NOT trust the behavior of this agent!
;;;          
;;;          
LABELS::C-ELEMENT*-0
> (toggle-burst-mode)
T
> (analyze 'c-element 'c-spec)
 
;;;
;;; Parameters set for speed-independent burst-mode analysis with trace verification
;;;
;;; Generating a trace-determinate specification from C-SPEC .....
;;;   ... minimized spec contains 4 states
;;;   ... successfully generated TD specification with 4 states
;;; Generating and trace verifying C-ELEMENT against St-C-SPEC*^0M3-0M3 .....
;;;
;;; SORT WARNING: Connected, unrestricted input/output `c' in C-ELEMENT*!
;;; Warning: Agent being redefined! (component C-ELEMENT*-18)
;;;          
 
 
;;;
;;; The top-level agent contains 23 unminimized states
;;;
;;;
;;;  Agent C-ELEMENT*-0M2 was successfully generated!
;;;
 
LABELS::C-ELEMENT*-0M2
> (delay-insensitive-mode)
NIL
> (analyze 'c-element 'c-spec)
 
;;;
;;; Parameters set for delay-insensitive burst-mode analysis with trace verification
;;;
;;; Generating a trace-determinate specification from C-SPEC .....
;;;   ... minimized spec contains 4 states
;;;   ... successfully generated TD specification with 4 states
;;; Generating and trace verifying C-ELEMENT against St-C-SPEC*^0M3-0M3 .....
;;;
;;; SORT ERROR: Isochronous Fork (2) input `b' to agent AND000*4^0 ... in C-ELEMENT*
;;; SORT ERROR: Isochronous Fork (2) input `a' to agent AND000*4^0 ... in C-ELEMENT*
;;; SORT ERROR: Isochronous Fork (2) input `c' to agent AND000*3^0 ... in C-ELEMENT*
;;; SORT WARNING: Connected, unrestricted input/output `c' in C-ELEMENT*!
 
 
;;;
;;; The top-level agent contains 23 unminimized states
;;; Warning: 
;;;          
;;;          3 errors encountered during creation of agent C-ELEMENT*-0M2.
;;;               Do NOT trust the behavior of this agent!
;;;          
;;;          
LABELS::C-ELEMENT*-0M2
> 

****** End of run transcript ******

The initial analysis is done using speed-independent analysis (where
isochronous forks are assumed).

Initially the C-element agent is generated without any constraints imposed
by its usage.  36 states are generated, and there is some internal
"computation interference".  This indicates that at certain points in the
state space, the AND or OR gates can be used inconsistently which could
result in hazards, run pulses, or deadlock.

To determine if these can happen in the prescribed C-element environment,
the specification "C-SPEC" is used.  (You can see its simple definition in
the file above.)  Speed-independent analysis results in 33 states, as 3 of
the states are non-reachable given the usage assumptions imposed by the
specification.  However, this implementation is NOT a speed-independent
implementation as computation interference exists.  Deadlocks exist in this
component, which are manifest in the physical implementation as runt
pulses.  If we walk through the first backtrace, we see how a static 1
hazard exists in this logic.  Inputs b and a became asserted, which
asserted the output 'c.  Note that the ab and bc AND gates have asserted,
but not the ac gate.  When b becomes unasserted, the ab and bc AND gates
unassert, which allows the OR gate to turn off.  This occurs before the ac
AND gate has turned on!  If the ac signal now changes, computation
interference occurs that could result in a static 1 runt pulse or hazard.
This tells us that this is not a speed-independent implementation of a
C-element.

This circuit is then verified under burst-mode assumptions.  I developed
this hazard model while working on the Post Office chip as slight loosening
of the speed-independent hazard model.  The assumption restricts inputs and
was based on engineering observation that nearly always holds in practical
implementations, yet achieves formal verification and synthesis of
asynchronous circuits.  This verification tool supports the burst-mode
stability requirement such that when all outputs have become asserted, no
inputs will be accepted until the circuit stabilizes.  (See references for
more details.)  This can be applied based on either a speed-independent or
delay-insensitive verification, but typically is used under the
speed-independent assumptions.  The stability assumption is local to the
asynchronous finite state machine (or agent) and can be easily verified by
timing analysis on a relatively local basis.

Burst-mode analysis of the C-element proves the implementation satisfies
the specification in 23 states.  A delay-insensitive analysis fails because
there are multiple isochronous forks specified in the implementation which
must be specified as "FORKS" for a delay-insensitive analysis.



LIMITATIONS



There are a number of inefficiencies and limitations in the code as it now
stands.  Following is a list of the major bugs:

  o There is no Null agent primitive.
     This is usually not a problem as deadlocks are bad in circuits!
     To define a deadlock, use an agent like "bi Null t.Null"  This is
     formally equivalent to a Null agent.
  o Verification assumes determinate trace systems.
     This may not always be the case, particularly without minimization.
     You may get a false negative until this bug is fixed.  (The solution
     is known, but not implemented yet.)
  o A "semi-modular" constraint not tested.
     When an input disables another enabled input we are not warned.
     This will show up in the composition checks if the cell is used
     hierarchically.
  o Nondeterministic transitions are not flagged as illegal.
     This may allow someone to think some implementations can arbitrate,
     when it is not the case.




COPYRIGHT




Copyright (C) 1992-1996 by 
  Kenneth S. Stevens

  Permission to use, copy, modify and/or distribute, but not sell, this 
  software and its documentation in source and binary forms for any
  purpose with or without modification is hereby granted without fee,
  subject to the following terms and conditions: 

 1. Redistributions of source code and documentation must retain the 
    above copyright notice, this list of conditions and the following
    disclaimer.

 2. Redistributions in binary form must reproduce the above copyright
    notice, this list of conditions and the following disclaimer in the 
    documentation and/or other materials provided with the distribution.

 3. All modifications to the source code must be clearly marked as such.  
    Binary redistributions based on modified source code must be clearly
    marked as modified versions in the documentation and/or other
    materials provided with the distribution.

 4. All advertising materials mentioning features or use of this software 
    must display the following acknowledgment: 
      This product includes software developed by Kenneth S. Stevens and
      other unpaid contributors.

 5. The name of Kenneth S. Stevens may not be used to endorse or promote
    products derived from this software without specific prior written
    permission.

 6. This software may not be called "Analyze" if it has been modified
    in any way, without the specific prior written permission of
    Kenneth S. Stevens. 

 7. THIS SOFTWARE IS PROVIDED BY KENNETH S. STEVENS AND CONTRIBUTORS 
 "AS IS" AND ANY EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT 
 LIMITED TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS FOR A
 PARTICULAR PURPOSE ARE DISCLAIMED.  IN NO EVENT SHALL KENNETH S. STEVENS 
 OR THE AUTHORS OF THIS SOFTWARE BE LIABLE FOR ANY DIRECT, INDIRECT, 
 INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES (INCLUDING, BUT 
 NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE GOODS OR SERVICES LOSS OF USE,
 DATA, OR PROFITS OR BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY
 THEORY OF LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT 
 (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT OF THE USE OF 
 THIS SOFTWARE, EVEN IF ADVISED OF THE POSSIBILITY OF SUCH DAMAGE. 

  Notes: 

  A.  Courtesy

  Our motivation in distributing this software freely is to encourage
  others to evaluate its effectiveness on a wider range of applications 
  than we have resources to attempt, and to provide a foundation for 
  further development of automatic synthesis techniques. 

  We would very much appreciate learning about other's experiences with 
  the system and suggestions for improvements.  Even more, we would
  appreciate contributions of two kinds: additional verification examples 
  that can be added to the distribution, and enhancements to the system.
  Although we do not promise to distribute the examples or enhancements,
  we may do so if feasible.

  B.  Historical Notes

  Analyze was designed in 1992-1994 by Kenneth S. Stevens at the
  University of Calgary.  It is based on Robin Milner's CCS.  Financial 
  support for the design and implementation of Analyze has come from 
  Hewlett-Packard Corporation.

  C.  Support, comments, feedback 

  If you need help or have comments or suggestions regarding the 3D
  system, please send electronic mail to "k.stevens@ieee.org".
  We do not have the resources to provide commercial-quality support,
  but we may be able to help you. 




REFERENCES



Milner, Robin.  "Communication and Concurrency", Prentice Hall
International (UK) Ltd, 1989.

Stevens, Kenneth S.  "Practical Verification and Synthesis of Low Latency
Asynchronous Systems", PhD Thesis, University of Calgary, Calgary, Alberta,
September 1994.

Stevens, Kenneth S.  "Automatic synthesis of Fast, Compact Self-Timed
State Machines", University of Calgary Research Report No. 92/495/33,
December 1992.

A. L. Davis, W. S. Coates, and K. S. Stevens.  "Automatic Synthesis of
Fast Compact Asynchronous Control Circuits", IFIP Working Conference on
Asynchronous Design Methodologies, March 1993.

Unger, Steven H. "Asynchronous Sequential Switching Circuits", 1983 Reprint
by Robert E. Krieger Publishing Company, Inc., Krieger Drive, Malabar,
Florida 32950  (originally published by Wiley, 1969)

Liu, Ying.  "Reasoning About Asynchronous Designs In CCS", Master's Thesis,
University of Calgary, Dept. of Computer & Electrical Engineering, October
1992.



COMPLIMENTS OF

Ken Stevens	k.stevens@ieee.org

	Source code can be ftp'ed from kdstevens.com:pub/stevens
	Files analyze.tar.gz and analyze-examples.tar

Analyze was developed at the University of Calgary, under a grant from
Hewlett-Packard Company.